Calibration and registration of multiple RGBD-Sensors

---
Introduction
- Joint coordinate system
- Virtual reconstruction for 3D telepresence
- Tracked checkerboard => correspondeces between camera space and worldspace
- Single calibration for each sensor, mapping all data in one step
- Tracking system coordinate system and World space coordinate system linked → reference

---
Introduction

---
Coordinate Systems & Spaces
- Joint World coordinate system W
- 3D-depth sensor coordinate system D + reference system D’
- 2D color camera coordinate system C + reference system C’
- Normalized 3D-volume space V as 3D-LookUp-Table

---
Parameters
- Intrinsic: principal point, focal length
- Extrinsic: Relation between color and depth
- Factory pre-calibration is not accurate enough

---
Calibration
- Initial calibration ​ɣ
- Generating the calibration volume
- Reference sampling
- Interpolation

---
Calibration

---
Initial calibration ɣ
- Intrinsic parameters with OpenCV
- Extrinsic calibration computed

---
Calibration Volume
- D normalized into volume space V
- Calibration volume initialized based on ɣ
- Accuracy of ɣ

---
Reference Sampling
- Tracked checkerboard on different locations
- Measures position in the volume Space V, point in the world space W, color coordinate in C
- Each sample r_i results correction tuple
  with

---
Interpolation
- Correction of the calibration volume at each v ∈ V
- Interpolating offsets in the local neighborhood of R
- Result: new calibration Ω with higher accuracy.

---
Interpolation
- K = number of neighbors
- Φ = weighing function
- Both depend on the used interpolation method
- Inverse distance weighting/ natural neighbor interpolation

---
Evaluation
- More accurate than any other method
- Scales with reference density
- Limited by hardware